## Slide 1: Embedded System Design
PROJECT 1 : SAFE DISINFECTING DEVICE
BÜŞRANUR YILMAZ

## Slide 2: PROJECT TOPIC
Using the Microwave Radar module, it is checked whether there are people or animals in sight.
When there is no moving person or animal, the UVC LED is activated and the UVC LED is turned on. Otherwise, the UVC LED remains off.
In this system, it is checked whether there is an object moving in the environment every 2 seconds.
Moving people or animal information and UVC LED status are sent to the server.

## Slide 3: SENSORS
Microwave Radar Module
VCC  3.3V
GND
OUT  ANALOG IN (PE3)
UVC LED
VCC  GPIO (PF1)
GND

## Slide 4: GENERAL SYSTEM DESIGN
UVC LED
Microwave Radar Module
Analog in
PE3
+3.3V
GND
GND
GPIO out
PF1

## Slide 5: PROJECT BLOCK DIAGRAM
HWI
(TIMER: ADC
Conversion is Started)
SWI
(ADC Value is Getting and Post by mailbox)
Main
(Initialize ADC and GPIO OUTPUT Configuration)
TASK
(UVC LED On/Off According to the ADC Value Sent by Mailbox)
TASK
(With the socket created in taskHercules, it is connected to the server from port 5011.)
TASK
(With the socket created in the functionTimer task, it is connected to the NTP server from port 37. Time data from 1900 until now is taken in seconds.
HERCULES
(Time data and UVC LED information displayed on HERCULES screen)

## Slide 6
TASK : taskLEDWrite
ADC values are between 0-4095.
If I read <10 UVC LED is ON. No people is around.
Otherwise UVC LED is OFF.
Post taskHercules task, send the UVC LED status information.
TASK : taskHercules
Socket is created.
Connect "192.168.1.30» with 5011 port.
Post the functionTimer task for geting time information.
Send time and led information to the server.
Task: functionTimer
Socket is created.
Connect "132.163.97.5» with 37 port.
Recv data from NTP server.
Calculate the seconds from 1/1/1990 and hold in global variable buffer[80]

## Slide 7: PROBLEMS
Setting the GPIO pin as input
Creating a Task and Socket
TASK synchronization
Receiving data from NTP Server